## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 4 Network Layer:
Data Plane
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
added new 8th edition material on middleboxes (and Internet arch), Net neutrality, buffering …
lighter header font
8.2 (July 2023), changes from 8.0:
some minor updates (e.g., IPv6 stats updated) but not much has changed.

## Slide 2: Network layer: our goals
understand principles behind network layer services, focusing on data plane:
  network layer service models
  forwarding versus routing
  how a router works
  addressing
  generalized forwarding
  Internet architecture
instantiation, implementation in the Internet
  IP protocol
  NAT, middleboxes

## Slide 3: Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
Middleboxes
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6

## Slide 4: Network-layer services and protocols
transport segment from sending to receiving host
  sender: encapsulates segments into datagrams, passes to link layer
  receiver: delivers segments to transport layer protocol
network layer protocols in every Internet device: hosts, routers
routers:
  examines header fields in all IP datagrams passing through it
  moves datagrams from input ports to output ports to transfer datagrams along end-end path
mobile network
enterprise
network
national or global ISP
datacenter
network
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical

## Slide 5: Two key network-layer functions
network-layer functions:
forwarding: move packets from a router’s input link to appropriate router output link
analogy: taking a trip
forwarding: process of getting through single interchange
forwarding
routing
routing: process of planning trip from source to destination
routing: determine route taken by packets from source to destination
  routing algorithms

## Slide 6: Network layer: data plane, control plane
Data plane:
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
Control plane
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
1
2
3
0111
values in arriving
packet header
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers

## Slide 7: Per-router control plane
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 8: Software-Defined Networking (SDN) control plane
Remote controller computes, installs forwarding tables in routers
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 9: Network service model
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing
Q: What service model for “channel” transporting datagrams from sender to receiver?

## Slide 10: Network-layer service model
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Service
Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
Loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
No guarantees on:
  successful datagram delivery to destination
  timing or order of delivery
  bandwidth available to end-end flow
Internet “best effort” service model
Quality of Service (QoS) Guarantees ?

## Slide 11: Network-layer service model
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Service
Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
Loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
Quality of Service (QoS) Guarantees ?

## Slide 12: Reflections on best-effort service:
simplicity of mechanism has allowed Internet to be widely deployed adopted
sufficient provisioning of bandwidth allows performance of real-time applications (e.g., interactive voice, video) to be “good enough” for “most of the time”
replicated, application-layer distributed services (datacenters, content distribution networks) connecting close to clients’ networks, allow services to be provided from multiple locations
congestion control of “elastic” services helps
It’s hard to argue with success of best-effort service model

## Slide 13: Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
Middleboxes

## Slide 14: Router architecture overview
high-level view of generic router architecture:
high-speed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame

## Slide 15: Router architecture overview
analogy view of generic router architecture:
roundabout
Station manager
entry stations
exit roads
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame
Notes: We can easily recognize the principal router components in Figure 4.4 in this analogy—the entry road and entry station correspond to the input port (with a lookup function to determine to local outgoing port); the roundabout corresponds to the switch fabric; and the roundabout exit road corresponds to the output port. With this analogy, it’s instructive to consider where bottlenecks might occur. What happens if cars arrive blazingly fast (for example, the roundabout is in Germany or Italy!) but the station attendant is slow? How fast must the attendant work to ensure there’s no backup on an entry road? Even with a blazingly fast attendant, what happens if cars traverse the roundabout slowly—can backups still occur? And what happens if most of the cars entering at all of the roundabout’s entrance ramps all want to leave the roundabout at the same exit ramp—can backups occur at the exit ramp or elsewhere? How should the roundabout operate if we want to assign priorities to different cars, or block certain cars from entering the roundabout in the first place? These are all analogous to critical questions faced by router and switch designers.

## Slide 16: Input port functions
switch
fabric
line
termination
physical layer:
bit-level reception
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
input port queuing: if datagrams arrive faster than forwarding rate into switch fabric
Frame
Datagram
Notes: Green box is a physical layer responsible for receiving bit level transmission. Copper, fiber wireless.
Link layer in blue – bit assemble into Ethernet frame. We will discuss this in details in chapter 6.
But most critical one, is here. Lookup, forwarding function. Lookup and forward is “Match plus action” behavior.
GOAL – processing at “line speed”, otherwise, buffer will be full and packet will be lost

## Slide 17: Input port functions
line
termination
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
physical layer:
bit-level reception
switch
fabric
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)

## Slide 18: Destination-based forwarding
Q: but what happens if ranges don’t divide up so nicely?
3
Notes: Text for this animation:
This all works out pretty nice and looks pretty simple!
But of course the devil is in the details, as the saying goes.
What happens, for example, when a subset of addresses say in this first range should go to say interface 3, rather than interface 0. Well, of course we could split the first address range into multiple pieces, and add in this new subrange with its new destination output port. But it turns out there’s a much simpler and elegant way to do this. Known as longest prefix matching.

## Slide 19: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
********
***
********
***
********
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
11001000 00010111 00010110 10100001

## Slide 20: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 21: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 22: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 23: Longest prefix matching
we’ll see why longest prefix matching is used shortly, when we study addressing
longest prefix matching: often performed using ternary content addressable memories (TCAMs)
  content addressable: present address to TCAM: retrieve address in one clock cycle, regardless of table size
  Cisco Catalyst: ~1M routing table entries in TCAM

## Slide 24: Switching fabrics
transfer packet from input link to appropriate output link
high-speed
switching
fabric
N input ports
N output ports
. . .
. . .
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
R
R
R
R
(rate: NR, ideally)

## Slide 25: Switching fabrics
bus
memory
memory
interconnection
network
three major types of switching fabrics:
transfer packet from input link to appropriate output link
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable

## Slide 26: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 27: Switching via a bus
datagram from input port memory to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access routers

## Slide 28: Switching via interconnection network
Crossbar, Clos networks, other interconnection nets initially developed to connect processors in multiprocessor
8x8 multistage switch
built from smaller-sized switches
3x3 crossbar
multistage switch: nxn switch from multiple stages of smaller switches
exploiting parallelism:
  fragment datagram into fixed length cells on entry
  switch cells through the fabric, reassemble datagram at exit
3x3 crossbar

## Slide 29: Switching via interconnection network
scaling, using multiple switching “planes” in parallel:
  speedup, scaleup via parallelism
fabric plane 0
. . .
. . .
fabric plane 1
. . .
. . .
fabric plane 2
. . .
. . .
fabric plane 3
. . .
. . .
fabric plane 4
. . .
. . .
fabric plane 5
. . .
. . .
fabric plane 6
. . .
. . .
fabric plane 7
. . .
. . .
Cisco CRS router:
  basic unit: 8 switching planes
  each plane: 3-stage interconnection network
  up to 100’s Tbps switching capacity

## Slide 30: Input port queuing
If switch fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
output port contention: only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward

## Slide 31: Output port queuing
Buffering required when datagrams arrive from fabric faster than link transmission rate. Drop policy: which datagrams to drop if no free buffers?
Scheduling discipline chooses among queued datagrams for transmission
Datagrams can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality
This is a really important slide
line
termination
link
layer
protocol
(send)
switch
fabric
(rate: NR)
datagram
buffer
queueing
R

## Slide 32: Output port queuing
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!

## Slide 33: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gbps link: 2.5 Gbit buffer
but too much buffering can increase delays (particularly in home routers)
  long RTTs: poor performance for real-time apps, sluggish TCP response
  recall delay-based congestion control: “keep bottleneck link just full enough (busy) but no fuller”
RTT C
.
N
more recent recommendation: with N flows, buffering equal to
Notes: You might think that more buffering is a good thing. Buffering is a bit like salt—just the right amount of salt makes food better, but too much makes it inedible!

## Slide 34: Buffer Management
buffer management:
drop: which packet to add, drop when buffers are full
  tail drop: drop arriving packet
  priority: drop/remove on priority basis
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
scheduling
marking: which packets to mark to signal congestion (ECN, RED)
R
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R

## Slide 35: Packet Scheduling: FCFS
packet scheduling: deciding which packet to send next on link
  first come, first served
  priority
  round robin
  weighted fair queueing
FCFS: packets transmitted in order of arrival to output port
also known as: First-in-first-out (FIFO)
real world examples?
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R

## Slide 36: Scheduling policies: priority
Priority scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
high priority queue
low priority queue
arrivals
classify
departures
link
1
3
2
4
5
arrivals
departures
packet in service
send packet from highest priority queue that has buffered packets
  FCFS within priority class
1
3
4
2
5
1
3
2
4
5

## Slide 37: Scheduling policies: round robin
Round Robin (RR) scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
classify
arrivals
departures
link
R
server cyclically, repeatedly scans class queues, sending one complete packet from each class (if available) in turn

## Slide 38: Scheduling policies: weighted fair queueing
Weighted Fair Queuing (WFQ):
generalized Round Robin
classify
arrivals
departures
link
R
w1
w2
w3
wi
Sjwj
minimum bandwidth guarantee (per-traffic-class)
each class, i, has weight, wi, and gets weighted amount of service in each cycle:

## Slide 39: Sidebar: Network Neutrality
What is network neutrality?
  technical: how an ISP should share/allocation its resources
  packet scheduling, buffer management are the mechanisms
  social, economic principles
    protecting free speech
    encouraging innovation, competition
  enforced legal rules and policies
Different countries have different “takes” on network neutrality

## Slide 40: Sidebar: Network Neutrality
2015 US FCC Order on Protecting and Promoting an Open Internet: three “clear, bright line” rules:
no blocking … “shall not block lawful content, applications, services, or non-harmful devices, subject to reasonable network management.”
no throttling … “shall not impair or degrade lawful Internet traffic on the basis of Internet content, application, or service, or use of a non-harmful device, subject to reasonable network management.”
no paid prioritization. … “shall not engage in paid prioritization”

## Slide 41: ISP: telecommunications or information service?
US Telecommunication Act of 1934 and 1996:
  Title II: imposes “common carrier duties” on telecommunications services: reasonable rates, non-discrimination and requires regulation
  Title I: applies to information services:
    no common carrier duties (not regulated)
    but grants FCC authority “… as may be necessary in the execution of its functions”4
Is an ISP a “telecommunications service” or an “information service” provider?
the answer really matters from a regulatory standpoint!

## Slide 42: Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Generalized Forwarding, SDN
  match+action
  OpenFlow: match+action in action
Middleboxes

## Slide 43: Network Layer: Internet
host, router network layer functions:
IP protocol
datagram format
addressing
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer
forwarding
table
Path-selection algorithms: implemented in
routing protocols (OSPF, BGP)
SDN controller

## Slide 44: IP Datagram format
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
IP protocol version number
header length(bytes)
upper layer protocol (e.g., TCP or UDP)
total datagram
length (bytes)
“type” of service:
diffserv (0:5)
ECN (6:7)
fragmentation/
reassembly
TTL: remaining max hops
(decremented at each router)
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead for TCP+IP
overhead
e.g., timestamp, record route taken
32-bit source IP address
32-bit destination IP address
header checksum
Maximum length: 64K bytes
Typically: 1500 bytes or less

## Slide 45: IP addressing: introduction
IP address: 32-bit identifier associated with each host or router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
dotted-decimal IP address notation:

## Slide 46: IP addressing: introduction
IP address: 32-bit identifier associated with each host or router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
dotted-decimal IP address notation:

## Slide 47: IP addressing: introduction
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Q: how are interfaces actually connected?
A: wired
Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
For now: don’t need to worry about how one interface is connected to another (with no intervening router)
A: we’ll learn about that in chapters 6, 7

## Slide 48: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
What’s a subnet ?
  device interfaces that can physically reach each other without passing through an intervening router
network consisting of 3 subnets
IP addresses have structure:
  subnet part: devices in same subnet have common high order bits
  host part: remaining low order bits

## Slide 49: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Recipe for defining subnets:
detach each interface from its host or router, creating “islands” of isolated networks
each isolated network is called a subnet
subnet mask: /24
(high-order 24 bits: subnet part of IP address)
subnet
223.1.3.0/24
subnet 223.1.1.0/24
subnet 223.1.2.0/24

## Slide 50: Subnets
where are the subnets?
what are the /24 subnet addresses?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1
subnet 223.1.1/24
subnet 223.1.7/24
subnet 223.1.3/24
subnet 223.1.2/24
subnet 223.1.9/24
subnet 223.1.8/24

## Slide 51: IP addressing: CIDR
CIDR: Classless InterDomain Routing (pronounced “cider”)
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 52: IP addresses: how to get one?
That’s actually two questions:
Q: How does a host get IP address within its network (host part of address)?
Q: How does a network get IP address for itself (network part of address)
How does host get IP address?
hard-coded by sysadmin in config file (e.g., /etc/rc.config in UNIX)
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 53: DHCP: Dynamic Host Configuration Protocol
goal: host dynamically obtains IP address from network server when it “joins” network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/on)
  support for mobile users who join/leave network
DHCP overview:
  host broadcasts DHCP discover msg [optional]
  DHCP server responds with DHCP offer msg [optional]
  host requests IP address: DHCP request msg
  DHCP server sends address: DHCP ack msg

## Slide 54: DHCP client-server scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
DHCP server
223.1.2.5
arriving DHCP client needs
address in this network
Typically, DHCP server will be co-located in router, serving all subnets to which router is attached

## Slide 55: DHCP client-server scenario
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I would like to use this IP address!
Broadcast: OK. You’ve got that IP address!
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]

## Slide 56: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 57: DHCP: example
Connecting laptop will use DHCP to get IP address, address of first-hop router, address of DNS server.
router with DHCP
server built into
router
DHCP REQUEST message encapsulated in UDP, encapsulated in IP, encapsulated in Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet de-mux’ed to IP de-mux’ed, UDP de-mux’ed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 58: DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulated DHCP server reply forwarded to client, de-muxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router

## Slide 59: IP addresses: how to get one?
Q: how does network get subnet part of IP address?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
ISP can then allocate out its address space in 8 blocks:
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 60: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing information:

## Slide 61: Hierarchical addressing: more specific routes
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
200.23.18.0/23
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Organization 1 moves from Fly-By-Night-ISP to ISPs-R-Us
ISPs-R-Us now advertises a more specific route to Organization 1
200.23.18.0/23
Organization 1
“or 200.23.18.0/23”

## Slide 62: Hierarchical addressing: more specific routes
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Organization 1 moves from Fly-By-Night-ISP to ISPs-R-Us
ISPs-R-Us now advertises a more specific route to Organization 1
200.23.18.0/23
Organization 1
“or 200.23.18.0/23”

## Slide 63: IP addressing: last words ...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned Names and Numbers http://www.icann.org/
  allocates IP addresses, through 5 regional registries (RRs) (who may then allocate to local registries)
  manages DNS root zone, including delegation of individual TLD (.com, .edu , …) management
Q: are there enough 32-bit IP addresses?
ICANN allocated last chunk of IPv4 addresses to RRs in 2011
NAT (next) helps IPv4 address space exhaustion
IPv6 has 128-bit address space
"Who the hell knew how much address space we needed?" Vint Cerf (reflecting on decision to make IPv4 address 32 bits long)

## Slide 64: Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Generalized Forwarding, SDN
  match+action
  OpenFlow: match+action in action
Middleboxes

## Slide 65: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network (e.g., home network) 10.0.0/24
138.76.29.7
rest of
Internet
datagrams with source or destination in this network have 10.0.0/24 address for source, destination (as usual)
all datagrams leaving local network have same source NAT IP address: 138.76.29.7, but different source port numbers
NAT: all devices in local network share just one IPv4 address as far as outside world is concerned

## Slide 66: NAT: network address translation
  all devices in local network have 32-bit addresses in a “private” IP address space (10/8, 172.16/12, 192.168/16 prefixes) that can only be used in local network
  advantages:
    just one IP address needed from provider ISP for all devices
    can change addresses of host in local network without notifying outside world
    can change ISP without changing addresses of devices in local network
    security: devices inside local net not directly addressable, visible by outside world

## Slide 67: NAT: network address translation
implementation: NAT router must (transparently):
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
      remote clients/servers will respond using (NAT IP address, new port #) as destination address
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in destination fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 68: NAT: network address translation
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1 sends datagram to 128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router changes datagram source address from 10.0.0.1, 3345 to 138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives, destination address: 138.76.29.7, 5001
10.0.0.1
10.0.0.2
10.0.0.3

## Slide 69: NAT: network address translation
NAT has been controversial:
  routers “should” only process up to layer 3
  address “shortage” should be solved by IPv6
  violates end-to-end argument (port # manipulation by network-layer device)
  NAT traversal: what if client wants to connect to server behind NAT?
but NAT is here to stay:
  extensively used in home and institutional nets, 4G/5G cellular nets

## Slide 70: IPv6: motivation
initial motivation: 32-bit IPv4 address space would be completely allocated
additional motivation:
  speed processing/forwarding: 40-byte fixed length header
  enable different network-layer treatment of “flows”

## Slide 71: IPv6 datagram format
payload (data)
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
priority: identify priority among datagrams in flow
flow label: identify datagrams in same "flow.” (concept of “flow” not well defined).
128-bit
IPv6 addresses
What’s missing (compared with IPv4):
no checksum (to speed processing at routers)
no fragmentation/reassembly
no options (available as upper-layer, next-header protocol at router)